## Slide 1: An alternative passenger transport model for SATIM
Théophile CROUZET 21/08/2019

## Slide 2
Cover of TIME , May 13, 2019
Photographer : Johnny Miller
Notes: Sure that you saw it, when I started my internship
not discuss about how bad it is or denounce someone
Illustrate perfectly how heterogenous the population is
= different consumption (energy) , access to facilities, activities, and so different mode of travel , behaviour and travel habits.
How measure it ?

## Slide 3: Introduction : SATIM
Energy demand
Economic constraints
Technological constraints
Energy supply least-cost solution
Transport
Industry
Agriculture
Residential
Commercial
Electricity
Liquid fuel
Demand sectors
Supply sectors
Notes: -powerful model which allows to generate energy systems and dynamics over a chosen time horizon
-relies on a demand-supply methodology. It takes into account economic constraints and technological constraints as fuel price, policies, new technologies, potential investment to compute an energy supply least-cost solution
-It has five demand sectors and two supply sectors

## Slide 4: Introduction : SATIM
SATIM
CGE model
Production and consumption functions
Expenditure on expansion plan
GDP
Household income
Notes: - Link model to provide long-term projection reducing uncertainties and to have economic feedback  exogenous demand , particularly for the transport because exogenous population projection

## Slide 5: Passenger demand calculation
Travel Time budget
Car ownership
Travel demand
Travel Speed
Car occupancy
Total population

## Slide 6: Transport demand sub-models
Vehicle parc model
Notes: In order to calculate the transport demand, the SATIM relies on different exogenous sub-models. We will focus on the passenger demand and not on the freight demand. The two sub-models I worked on are the time budget model and the passenger demand model.

## Slide 7: Time budget model calibration
Time budget model
Vehicle parc model
Access to vehicle
Travel time
Private and public speeds
Vehicle occupancy
Travel time budget split
Assumptions
Calibrated parameters
Total vehicles
Total private and public pkm
Total vehicle-km
Checks
Vehicle mileage by income group

## Slide 8: Passenger demand model
Access to vehicle
Travel time
Private and public speeds
Vehicle occupancy
Travel time budget split
Vehicle mileage by income group
Passenger demand model
Populations projections by income group
Time budget model
CGE model
Projected vehicle-km and pkm by mode segment

## Slide 9: NHTS 2013 data update calibration
Access to vehicle
Travel time budget
Private and public speeds
Vehicle occupancy
Travel time budget split
Travel days
Update the parameters
Remove the assumptions

## Slide 10: NHTS 2013 data update calibration
Access to vehicle
Travel time budget
Private and public speeds
Vehicle occupancy
Travel time budget split
Travel days
Income group | Low | Middle | High
old TTB (hours) | 1.10 | 1.10 | 1.10
New TTB (hours) | 1.32 | 1.35 | 1.39
Notes: TTB = number of hours people are likely to travel in a day
International studies = stable, constant for all the world population
but at a disaggregated level no longer valid. Richest people can afford different activities. It’s not about speed because according to the studies … but it is about money !
confirmed by NHTS values
- People travel more, or longer : because of low density cities ?

## Slide 11: NHTS 2013 data update calibration
Income group | low | Middle | High
Old values (days) | 300 | 300 | 300
New values (days) | 201 | 232 | 284
Access to vehicle
Private and public speeds
Travel time budget split
Travel days
Vehicle occupancy
Notes: Same phenomenon + low income more likely to be unemployed .

## Slide 12: NHTS 2013 data update calibration
Vehicle occupancy
Income group | low | Middle | High | RSA
Old values (per/car) | 1.4 | 1.4 | 1.4 | 1.4
New values (per/car) | 3.21 | 2.30 | 1.47 | 1.68
Access to vehicle
Private and public speeds
Travel time budget split
Data from Roux et al. 2002 (Cape Town) | 
Average car occupancy (per/car) | 1.83
Notes: -full assumption , quite different from the South African studies.

## Slide 13: NHTS 2013 data update calibration
Access to vehicle
Income group | low | Middle | High
Old values (% of population) | 2% | 53% | 78%
New values (% of population) | 12% | 27% | 78%
Private and public speeds
Travel time budget split

## Slide 14: NHTS 2013 data update calibration
Private and public speeds
Old public speed (km/hours) | 21.7
New public speed (km/hours) | 24.5
Old private speed (km/hours) | 33.2
new private speed (km/hours) | 39
Travel time budget split
Data from Hitge et al. 2015 (Cape Town) | 
private speed (km/hours) | 38.4
public speed (km/hours) | 27.4

## Slide 15: NHTS 2013 data update calibration
Travel time budget split
Income group | low | Middle | High
Old values (% trips using private mode) | 25% | 52% | 80%
New values (% trips using private mode) | 46% | 74% | 84%

## Slide 16: Data update results
Chart: Base year private vehicle mileage comparison
| Reference | National approach | Provincial approach
Low income | 8.03 | 5.46
Middle income | 13.42 | 8.67
High income | 15.66 | 16.58

## Slide 17: Data update results
Chart: Total priv.veh projections
| 2012 | 2015 | 2020 | 2030 | 2040 | 2050 | 2012 | 2015 | 2020 | 2030 | 2040 | 2050 | Reference | New data
Low Income | 0.1172 | 0.11299 | 0.11096 | 0.098399 | 0.072489 | 0.060154 | 0.57395 | 0.55333 | 0.54338 | 0.48188 | 0.35499 | 0.29459
Middle Income | 2.8163 | 2.8771 | 3.0515 | 3.3271 | 3.8626 | 4.2584 | 1.1656 | 1.1908 | 1.2629 | 1.377 | 1.5986 | 1.7625
High Income | 4.0841 | 4.7098 | 5.3036 | 7.5143 | 10.1113 | 11.5345 | 4.917 | 5.6703 | 6.3851 | 9.0467 | 12.1733 | 13.8867

## Slide 18: Data update results
Chart: Passenger-km demand (billions of pass.km) projection by year
| 2015 | 2020 | 2030 | 2040 | 2050 | 2015 | 2020 | 2030 | 2040 | 2050 | Reference | New data
Car | 136.9345 | 150.9447 | 197.0408 | 254.5091 | 287.6876 | 146.5726 | 162.4602 | 218.6043 | 285.2419 | 322.6383
SUV | 18.2708 | 20.1402 | 26.2907 | 33.9585 | 38.3854 | 19.5568 | 21.6767 | 29.1678 | 38.0591 | 43.0488
Motorbike | 4.1522 | 4.577 | 5.9747 | 7.7173 | 8.7233 | 4.0644 | 4.505 | 6.0619 | 7.9097 | 8.9467
Bus | 14.3636 | 14.1694 | 16.6582 | 12.2739 | 7.6476 | 15.3228 | 15.2397 | 18.5275 | 14.4829 | 9.883
Minibus | 97.552 | 96.233 | 91.4602 | 78.6732 | 69.3383 | 104.0664 | 103.5018 | 101.7235 | 92.8321 | 89.6063
BRT | 0.6016 | 5.4054 | 12.5469 | 22.3041 | 32.1047 | 0.50516 | 5.7592 | 13.2685 | 23.5052 | 33.7774
Metro Rail | 15.5095 | 15.2998 | 11.3494 | 11.818 | 13.5857 | 16.5452 | 16.4555 | 12.623 | 13.9449 | 17.5569
Gautrain | 0.68614 | 0.74106 | 0.9302 | 1.1255 | 1.2136 | 0.85467 | 0.92429 | 1.1711 | 1.4205 | 1.5297

## Slide 19: Current population subdivision
Total population
Low income group
Access to car
No access to car
Medium Income group
Access to car
High income group
No access to car
Access to car
No access to car

## Slide 20: Why disaggregate the demand ?
Geographical location | Population (millions of persons) | Private vehicle mileage ('000km/year/veh) | Private vehicles total (millions of vehicles)
Rural | 19.48 | 10.89 | 0.77
Urban | 33.55 | 14.35 | 5.27

## Slide 21: Why disaggregate the demand ?
Chart: South African urbanisation
| 2012 | 2015 | 2020 | 2030 | 2040 | 2050
Rural population share | 19.4769 | 19.1652 | 18.42 | 16.9967 | 15.1744 | 13.2201
Urban population share | 33.5531 | 35.3248 | 38.0115 | 43.8469 | 48.536 | 52.2143

## Slide 22: Why disaggregate the demand ?
Chart: Car occupancy accross South African provinces
| Western Cape | Eastern Cape | Northern Cape | Free State | KwaZulu-Natal | North West | Gauteng | Mpumalanga | Limpopo
 | 1.5988 | 2.0221 | 2.0898 | 1.5392 | 1.9777 | 1.8372 | 1.5285 | 1.7201 | 2.3876
Chart: 
| Western Cape | Eastern Cape | Northern Cape | Free State | KwaZulu-Natal | North West | Gauteng | Mpumalanga | Limpopo
Access to car across South African provinces | 0.44781 | 0.20879 | 0.2237 | 0.3003 | 0.24198 | 0.26718 | 0.44662 | 0.26593 | 0.2479

## Slide 23: Why disaggregate the demand ?
Chart: Main mode of travel to place of employement across provinces
| Western Cape | Eastern Cape | Northern Cape | Free State | KwaZulu-Natal | North West | Gauteng | Mpumalanga | Limpopo
Train | 0.13266 | 0.013181 | 0.00055835 | 0.00030664 | 0.02927 | 0 | 0.073622 | 0.0019984 | 0.00022566
Bus | 0.072322 | 0.030705 | 0.034002 | 0.060061 | 0.068987 | 0.13424 | 0.051294 | 0.2108 | 0.1109
Taxi | 0.15086 | 0.2887 | 0.1272 | 0.24249 | 0.3579 | 0.27519 | 0.3039 | 0.19831 | 0.19082
Car/bakkie/truck/lorry driver | 0.35443 | 0.24322 | 0.2544 | 0.27559 | 0.25063 | 0.22781 | 0.3808 | 0.24563 | 0.24795
Car/bakkie/truck/lorry passenger | 0.10753 | 0.085037 | 0.14064 | 0.073051 | 0.071595 | 0.074713 | 0.058942 | 0.069331 | 0.085887
Walking all the way | 0.16849 | 0.33355 | 0.4217 | 0.3225 | 0.21285 | 0.26447 | 0.12163 | 0.25952 | 0.34374
Other | 0.013701 | 0.0056043 | 0.021503 | 0.026006 | 0.0087625 | 0.023577 | 0.0098177 | 0.014409 | 0.020487

## Slide 24: Disaggregation
Total population
Rural area
Urban area
Western Cape
Eastern Cape
Northern Cape
Free State
KwaZulu-Natal
North West
Gauteng
Income quintile 1
Income quintile 2
Income quintile 3
Income quintile 4
Income quintile 5
Access to car
No access to car
Mpumalanga
Limpopo

## Slide 25: New population projections
Growth rates per quintiles and per geographical location
Population distribution for the year y-1
Total population by income group
Total population by geo. location
CGE model
World
Bank data
Population distribution for the year y

## Slide 26: New population projection
Chart: Population projections comparison
| 2015 | 2020 | 2030 | 2040 | 2050 | 2015 | 2020 | 2030 | 2040 | 2050 | Reference | Disaggregated approach
Low income | 22.5978 | 22.1914 | 19.6798 | 14.4978 | 12.0309
Middle income | 17.3369 | 18.3876 | 20.0484 | 23.2754 | 25.6606
High income | 14.5557 | 15.8555 | 21.1155 | 25.9421 | 27.7482
Quintile 1 | 0 | 13.5566 | 13.3104 | 11.804 | 8.6958 | 7.2162
Quintile 2 | 0 | 12.5321 | 12.5808 | 11.9139 | 10.4854 | 9.9781
Quintile 3 | 0 | 10.1537 | 10.769 | 11.7417 | 13.6317 | 15.0286
Quintile 4 | 0 | 9.4609 | 10.1998 | 12.6374 | 15.2372 | 16.461
Quintile 5 | 0 | 8.7867 | 9.5714 | 12.7466 | 15.6603 | 16.7506

## Slide 27: Base year calibration comparison
Chart: 2012 Base year passenger-km demand (billions of pass.km) by mode comparison
| Car | SUV | Motorbike | Bus | Minibus taxi | BRT | Metro Rail | Gautrain
National approach | 130.8634 | 17.4608 | 3.6288 | 15.1011 | 102.5607 | 0.47532 | 16.3058 | 0.76723
Provincial approach | 118.0356 | 15.7492 | 3.2731 | 15.1641 | 102.9884 | 0.80361 | 16.3738 | 1.2671

## Slide 28: Total vehicle parc projection
Chart: Total Private vehicles
| 2012 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2030 | 2040 | 2050
eNAtis data | 6.11 | 6.84 | 7.01 | 7.17 | 7.34 | 7.42
Provincial approach | 6.0841 | 6.747 | 7.4277
National approach | 6.6964 | 7.4555 | 8.2342
Reference | 7.0564 | 7.7399 | 8.5076
Notes: Add reference case

## Slide 29: Total vehicle parc projection
Chart: Private vehicles projections comparison
| 2012 | 2015 | 2020 | 2030 | 2040 | 2050 | 2012 | 2015 | 2020 | 2030 | 2040 | 2050 | 2012 | 2015 | 2020 | 2030 | 2040 | 2050 | Reference | National approach | Provincial approach
Low income | 0.1172 | 0.11299 | 0.11096 | 0.098399 | 0.072489 | 0.060154 | 0.57395 | 0.55333 | 0.54338 | 0.48188 | 0.35499 | 0.29459
Middle income | 2.8163 | 2.8771 | 3.0515 | 3.3271 | 3.8626 | 4.2584 | 1.1656 | 1.1908 | 1.2629 | 1.377 | 1.5986 | 1.7625
High income | 4.0841 | 4.7098 | 5.3036 | 7.5143 | 10.1113 | 11.5345 | 4.917 | 5.6703 | 6.3851 | 9.0467 | 12.1733 | 13.8867
Quintile 1 | 0 | 0.25561 | 0.24702 | 0.24533 | 0.22052 | 0.16365 | 0.1385
Quintile 2 | 0 | 0.36625 | 0.35961 | 0.36552 | 0.35111 | 0.31138 | 0.30223
Quintile 3 | 0 | 0.65133 | 0.66649 | 0.71259 | 0.78395 | 0.91441 | 1.0201
Quintile 4 | 0 | 1.2941 | 1.4218 | 1.5379 | 1.9122 | 2.3098 | 2.5067
Quintile 5 | 0 | 3.4769 | 4.0109 | 4.5236 | 6.42 | 8.6462 | 9.8838
Notes: Mention numbers

## Slide 30: Passenger-km demand
Chart: Public vs private pass.km projections
| 2015 | 2020 | 2030 | 2040 | 2050
Reference - Private transport | 159.3575 | 175.6619 | 229.3061 | 296.1849 | 334.7963
Reference - Public transport | 114.3492 | 117.6793 | 116.2867 | 113.9208 | 116.2424
National approach - Private transport | 170.1939 | 188.6418 | 253.834 | 331.2107 | 374.6339
National approach - Public transport | 121.9715 | 126.6407 | 128.7861 | 131.7027 | 142.4703
Provincial approach - Private transport | 152.2305 | 167.7847 | 220.6291 | 281.5289 | 316.1239
Provincial approach - Public transport | 123.8938 | 132.0279 | 136.219 | 145.8576 | 157.423

## Slide 31: Fuel consumption
Chart: Diesel consumption comparison
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Reference | 1461.4173 | 1974.2782 | 2859.5801 | 4392.3885 | 5827.5591 | 7205.5118 | 7356.9554 | 7923.3596
National Approach | 1393.4383 | 1893.7008 | 2710.4987 | 4052.4934 | 5716.0105 | 7364.042 | 7486.0892 | 7991.8635
Provincial approach | 1283.4646 | 1396.063 | 2143.5696 | 3251.4436 | 4875.5906 | 6202.6247 | 6273.2283 | 6645.1444
Chart: Gasoline consumption comparison
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Reference | 9562.2807 | 9401.7544 | 9419.883 | 8051.7544 | 6040.9357 | 4026.9006 | 2821.0526 | 2572.5146
National approach | 8808.4795 | 8650.5848 | 8607.6023 | 7446.7836 | 5769.883 | 3948.2456 | 2833.3333 | 2560.5263
Provincial approach | 7873.3918 | 8080.9942 | 7850 | 6861.1111 | 4978.3626 | 3322.5146 | 2380.117 | 2115.7895

## Slide 32: Thank you for listening ! Any questions ?