## Slide 1: Energy modelling with TIMES
Slides by Uwe Remme, IEA, adapted for ERC by Bruno Merven
September 2016

## Slide 2: Content
Overview of TIMES
The Core equations
Building blocks of a TIMES model
Solving the TIMES model using LP/MIP

## Slide 3: TIMES
Advanced Features/Variants
Multi-regional
Vintaging
Elastic demands
Endogeneous learning
Discrete capacity expansion
Early retirement of capacity
Macroeconomic linkage
Climate extension
Stochastic programming
Alternative objective functions
Multi-criteria optimization
Methodology
Bottom-up Model
Perfect competition
Perfect foresight (or myopic)
Optimization (LP/MIP/NLP)
Min/Max Objective function
s.t.
Equations, Constraints
Decision Variables <=> Solution
Input parameters
Development
By ETSAP (Energy Technology Systems Analysis Program; www.iea-etsap.org)
Implementation in GAMS
Model generator
Two software interfaces available: ANSWER-TIMES and VEDA-FE
TIMES
(The Integrated MARKAL
EFOM System)

## Slide 4: Applications of MARKAL/TIMES around the world
Used by more than 150 institutions in 63 countries
Contracting parties
Model users

## Slide 5: Core Equations of a TIMES model

## Slide 6: TIMES Basic model constraints based on fundamental principles
Energy conversion
Transformation equation
Flows through technology limited by available capacity
Capacity-utilisation constraint
Energy conservation
Commodity balance
TIMES equivalent
Principle
Flow variables
Decision variables
New capacity variables
Activity variables
Objective function:
Minimise system costs
Cost coefficients of decision variables

## Slide 7: Basic equations
EQ(l)_COMBAL r,t,c,s Commodity balance
EQ_ACTFLO r,v,t,p,s Definition of activity variable
EQ_CAPACT r,v,t,p,s Utilization constraint
EQ_PTRANS r,v,t,p,cg1,cg2,s Transformation equation
EQ_OBJ Objective function

## Slide 8: Commodity balance equation
Imports
VAR_IRE
Exports
VAR_IRE
Production
VAR_FLO
Consumption
VAR_FLO
Output storage
VAR_SOUT
Input storage
VAR_SIN
Capacity related commodity flows
NCAP_COM(r,v,p,com,‘in‘) x VAR_CAP
Capacity related commodity flows
NCAP_COM(r,v,p,com,‘out‘) x VAR_CAP
Auxiliary emission of exchange process
IRE_FLOSUM x VAR_IRE
Auxiliary production of exchange process
IRE_FLOSUM x VAR_IRE
Commodity required at investment
NCAP_ICOM(r,v,p,c) x VAR_NCAP
Commodity released at decommissioning
NCAP_OCOM(r,t,p,c) x VAR_NCAP
COM


Production
Consumption
Commodity type MATerial, FINancial
Commodity type NRG, ENV, DEM
Projected demand
COM_PROJ(r,t,c)

## Slide 9: Definition of activity variable
Activity variable VAR_ACT measures generation of the technology.
In most cases one of the energy output flows; for power plants activity equals the electricity output flow
ELC
COL
Supercrititcal
coal plant (SCP)
CO2
Flows

## Slide 10: Capacity utilization constraint
Activity of process
Three availabilities:
NCAP_AFA(r,v,p,l) : Annual availability
NCAP_AFS(r,v,p,s,l) : Seasonal availability
NCAP_AF(r,v,p,s,l) : Availability for individual timeslices
which can be combined.
Capacity:
Past investments before model horizon
New capacity built in previous periods
New capacity built in current period t


Available capacity of process p in period t and timeslice s
VAR_ACT(r,v,t,p,s)
EQ(l)_CAPACT r,v,t,p,s

## Slide 11: Transformation equation
Transformation equations establishes relationship between the input and output flow.
ELC
GAS
Gas power plant
EGASCC0
VAR_FLOELC
VAR_FLOGAS
Transformation equation
Overall efficiency from input to output

## Slide 12: Objective function
Objective function = total discounted energy system costs over the entire model horizon
Typical cost components in the objective function:
  Variable O&M costs in period t
  Fixed O&M costs in period t
  Levelized investment costs in period t (capital recovery factor crf depends on economic lifetime and/or technology specific discount rate)
  Costs/Revenues from imports/exports in period t
Costs in real terms
General discount rate used to discount costs from different periods to base year
Investment costs spread over construction time to mimick interest cost during construction

## Slide 13: Further model equations
Description of exchange processes in multi-regional models
Elastic demands
Product/market share constraints, e.g. share of hydrogen cars in total person kilometer demand
Peaking equation: Ensures enough available firm capacity during peak demand
Storage equation: Modeling of storage between timeslices (e.g. pump storage) or between periods (e.g. stockpiling)
Commodity-specific availabilities, e.g. full load hours of CHP plant in backpressure and condensing mode
User constraints: Flexible framework to formulate constraints being not part of the standard portfolio of TIMES equations, e.g. growth constraints, renewable quota

## Slide 14: Building Blocks of TIMES model

## Slide 15: TIMES model components
Made up of 2 simple components:
  1. Energy Carriers (e.g. fuels, demand)
  2. Technologies (e.g. Light bulb, power plant) all characterized in the same way:
  Input and Output Carriers
  Efficiency
  Investment Costs per unit of capacity
  Activity Costs
  Existing Capacity
  Annual Availability
  Expected Life
  Emissions

## Slide 16: Technology representation
Electricity
Coal
Supercrititcal
coal plant (SCP)
CO2
Process
Commodities
Flows
Flows
Coal PC Supercrit. | Unit | 2005 | 2010 | 2020 | 2030
Size | MWel | 600 | 600 | 600 | 600
Construction time | Years | 3 | 3 | 3 | 3
Lifetime | Years | 35 | 35 | 35 | 35
Efficiency (LHV) | % | 46 | 47 | 48 | 50
Max. availability | h/a | 7500 | 7500 | 7500 | 7500
Spec. Investment costs (overnight) | €/kWel | 1175 | 1175 | 1140 | 1140
Fixed O&M | €/(kW a) | 40.5 | 40.5 | 40.5 | 40.5
Var. O&M | €/MWhel | 2.6 | 2.6 | 2.6 | 2.6
2.2 kWh
1 kWh
0.27 kgSKE
0.736 kg
Efficiency eqn
Emission eqn
Activity definition
Utilization eqn
Plant efficiency
CO2 Emission factor
Annual availability
Input parameter

## Slide 17: Horizontal dimension of the RES: technology chains
Electricity HV
Coal, power
CO2
Supercritical
coal plant
Coal
transport
Grid HV &
Transf.
Lighting
Urban trains
Industry
Domestic
mining
Coal
imports
Grid MV &
Transf.
Coal, washed
Electricity MV
Electricity LV
Appliances
Backward Loops

## Slide 18: Vertical dimension of the RES: competition
Electricity HV
Coal, power
CO2
Supercritical
coal plant (exst)
Coal
transport
Grid HV &
Transf.
Lighting
Urban trains
Industry
Domestic
mining
Coal
imports
Grid MV &
Transf.
Coal, washed
Electricity MV
Appliances
Ultrasupercritical
coal plant (new)
Natural gas
GT (exist)
Natural gas
CC (new)
Natural gas
Lignite
Supercritical
lignite plant (exst)
Supercritical
lignite plant (new)
Competing options to produce
electricity:
between technologies
between old and new plants
Influenced by:
Technology costs
Efficiencies
Emission factors
Fuel prices…

## Slide 19: Solving the TIMES model

## Slide 20: Linear programming (LP) model
Optimization problem
Decision variables (positve, continuous):
Activity variables (Production level of technologies)
Energy flows
Investment decisions
Model constraints
(linear constraints):
Energy/ emission balances
Efficiency relationships
Utilization constraints
Peaking eqn (reserve capacity)
GHG mitigation targets, quota for renewables,…
Objective function
Min
Standard TIMES model: Linear programming
Implemented in modeling environment GAMS (General Algebraic Modeling System) for optimization/equilibrium problems
Solution by interior point solvers (CPLEX, XPRESS)
Variants of TIMES:
  Macro economic module -> Non-linear eqns -> Non-linear programming
  Block-wise capacity expansion -> Binary variables -> Mixed-integer programming

## Slide 21: ANSWER interface

## Slide 22: ANSWER-TIMES: Model interface

## Slide 23: ANSWER-TIMES: Data and results screen

## Slide 24: ANSWER-TIMES: RES navigation

## Slide 25: TIMES Installation: 4 Steps
Vula Resources: TIMES – GAMS folder
Install TIMES:in the Answer_TimesSetup_6.7.8 folder:
  Run “setupAnswerTimes6.7.8.exe”
Install GAMS:in the TIMES – GAMS folder
  Run either: GAMS_windows_x86_32 or GAMSsetupWinx64_64.exe
Copy Licenses: in the Licenses folder
  TIMES: unzip answerTIMESv6_Course2014Aug.zm9 into C:\AnswerTIMESv6
  GAMS: copy gamslice.txt file into GAMS folder
Add GAMS folder to path:
Choose Start, Control Panel, and then choose System and Security. Click on the “System” option and then click on the “Advanced system settings” option. This will bring up the System dialogue box, with the Advanced tab selected. Click on the Environment Variables button at the lower right. Scroll down in the System variables list until you find Path, select Path and then click on the Edit button to bring up the Edit System Variable form. (If you find that the Edit button is disabled, ask your system administrator to change the Path for you.) Then if your GAMS installation directory is say C:\Program Files\GAMS23.3, add the following to the end of what is currently displayed as the Value of Path:
;C:\”Program Files\GAMS23.3”
Note that there must not be any intervening space between the last character of the current Path and the semicolon, and also the drive letter (C) must be capital. Click on the OK button to confirm the new Path. Reboot the PC so that the new Path takes effect.

## Slide 26: Tiny TIMES model: pdf file in TIMES – GAMS folder