## Slide 1: An Overview of the SA TIMES Model SATIM
Bruno Merven
September 2016

## Slide 2: SATIM – Key Points
South African TIMES Model (SATIM)
Partial equilibrium linear optimisation model capable of representing the whole energy system, including its economic costs and its emissions.
A number of years of development - 2003 IEP, 2007 LTMS, 2011 LEP -> current version
Methodology, Assumptions and Models in the public domain: http://energydata.uct.ac.za
https://ercviz.shinyapps.io/gdxplore/ (beta version of results vizualisation)
TIMES code is Open Source and has an active development community (IEA-ETSAP)!

## Slide 3: SATIM: Main Features
Bottom-up Energy Systems Optimization Long-Range (>10 years) Planning Model (similar to the one used for the IEP)
Full Sector: Includes and allows trade-off between demand and Supply
End-use type model:
  Gives a detailed description of how the energy is used.
  Describes the types of equipment used and how much energy is used by each type of equipment to satisfy demand.
  Can be used to forecast useful energy as well as final energy demand
  Allows for exploration of policy impacts (via constraints/targets, subsidies and taxes)
  Can capture:
    structural changes/ shocks
    mode switching (transport)
    fuel switching
    Technical improvement/ improved efficiency
    Intensity changes e.g. mines have to dig deeper

## Slide 4: The Full Energy Chain is Characterised

## Slide 5: Simple Reference Energy System

## Slide 6: Overview of SATIM and data needs
  Inputs to optimization model
  Outputs from optimization model
  Intermediary information flow
Economic Analysis
Demand Sectors (commercial and agriculture omitted from diagram)
MARKAL/TIMES optimization energy model (GAMS with CPLEX solver)
Base Year Energy Balance
Residential sector Demand projections
Industrial sector future technologies
Industrial sector Demand projections
Transport sector future technologies
Transport sector Demand projections
Supply Technology
Existing power system
Existing liquid fuel supply system
Socio-Economic Variables (GDP, Population)
Energy Resources/Import and Exports
Residential sector future technologies
Policy objectives/constraints
Socio-economic growth objectives
Environmental objectives, taxes
Energy security objectives
Future power generation technologies
Existing coal/gas supply system
Future coal/gas supply technologies
Future liquid fuel supply technologies
Fossil fuel reserves
Renewable energy resource potential
Import/export (elc, oil, gas)
Residential sector base-year calibration
Results Analysis
Industrial sector base-year calibration
Transport sector base-year calibration
Investment Schedule/Plan
Imports, exports, consumption, production, Emissions
System costs, energy costs
Objective function = minimize sum of total discounted costs over planning horizon
Given constraints and other system parameters (cost, efficiency, load curves, etc.)

## Slide 7: Sectors
Sector | Disaggregation | Driver
Agriculture | By end use: irrigation, transport etc | Agriculture GDP
Residential | High, medium and low income/ electrified and non-electrified | Population, Household income, electrification
 | By end use: cooking, lighting etc | 
Commercial | By end use: lighting, HVAC, etc | Commercial GDP, building stock
Industrial | By sector: Iron and Steel, Pulp and paper etc | Sectoral Value Added or Output
 | By end use: thermal fuel or electricity (compressed air, cooling, motive, etc | 
Transport | By Sector: Air, Freight, Passenger, Pipeline | Transport GDP, Population and household income
 | By end use - Freight: rail, road (light, medium, heavy) | 
 | By end use – Passenger: Cars, SUV, bus, etc… | 

## Slide 8: Variation of the Load (electricity)
Default: 20 Time-slices
Year divided in 3 seasons
Each season represented by 2 typical days
Season 1 and 3 (summer), each day is broken up into 3 parts (night, day, evening)
Season 2 (winter) week day is broken up into 5 parts (night, morning, afternoon, evening, peak)

## Slide 9: Current Projects

## Slide 10: Project: Transport Study Phase 2 Scope: National E3 focus on transport (and upstream) policies Focus: Transport Funders: DST via SANEDI

## Slide 11: Project: Fuel Switching Project Scope: National E3 Focus: focus on transmission and distribution parameters and spatial aspects of demand Funders: DST via SANEDI

## Slide 12: Flexible Demand Project: Overall
Pre-Winter
Winter
Post-Winter
Project: Flexible Demand Project Scope: National E3 Focus: focus on time of use of electricity Funders: DST via SANEDI

## Slide 13: Flexible Demand Project: Industry

## Slide 14: Flexible Demand Project: Residential

## Slide 15: Flexible Demand: Commerce

## Slide 16: Link to Economy-wide model
EN
EC
Technology Mix
Electricity Price
Electricity Production function
Expenditure on expansion plan
Production function of all activities (energy)
Consumption function of households (energy)
GDP
Welfare
Employment
GDP
Household income
Price indices
Energy/Climate Policy

## Slide 17
CKAN (Open Knowledge Foundation)
Free, open source and maintained
Community based and access controlled
International state of the art, including linked data and research citations (DOI referencing)
Flexible and reproducible
https://energydata.uct.ac.za, https://ercviz.shinyapps.io/gdxplore/ (beta version)
Project: Energy Data Portal Focus: Energy Data Funders: DST via SANEDI

## Slide 19
Data Objectives
Immediate / temporary
Establish a data culture at the ERC
Share input data and information
Make ERC energy models easily accessible
Improve version control and model reproducibility
Pilot and feedback
Future
Create a data community around energy modeling
Establish a model data archive to feed into future data portals
Provide data visualisations
Close the gap from modeling to decision making

## Slide 20: Recent Projects

## Slide 21: Project: Deep Decarbonisation Development Pathways (DDPP) Scope: National E3 Focus: Climate Change, Economy, Social Funders: IDDRI, CIFF Collaborators: ERC-E2C2
D
High skill
Low skill
High intensity
Low intensity
C
B
EN
EN-el
EC
Cumulative CO2 Constraint
GDP
Household Income
(soft link)
CO2 Trajectory
for Power Sector
(soft link)
Power Plant Mix
GDP
Welfare
Employment
Electricity Price
Electricity Production function
Expenditure on expansion plan
Electricity Demand
(Altieri et al. 2016)

## Slide 22: Project: Deep Decarbonisation Development Pathways (DDPP) Scope: National E3 Focus: Climate Change, Economy, Social Funders: IDDRI, CIFF Collaborators: ERC-E2C2
Chart: Unemployment Rate
| 2007 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Scenario 1 Economic Structure | 0.236 | 0.23875 | 0.24193 | 0.27228 | 0.2901 | 0.29789 | 0.26817 | 0.23022 | 0.18174 | 0.11815
Scenario 2 High Skills | 0.236 | 0.24108 | 0.25317 | 0.29577 | 0.32283 | 0.33621 | 0.31182 | 0.2782 | 0.23409 | 0.17764
Chart: Energy Related CO2-eq Emissions
| 2010 | 2050 | 2050 | Economic Structure Scenario 1 | High Skills Scenario 2
Electricity | 225.7613 | 11.1186 | 11.4156
Industry | 50.5175 | 81.3 | 86.508
Transportation | 55.8726 | 70.3522 | 67.1171
Buildings | 13.498 | 27.9609 | 26.8133
Agriculture | 3.7299 | 16.1582 | 7.4002
CTL, GTL, Refineries | 48.3929 | 34.4385 | 42.2915

## Slide 23: Project: Uncertainty in baseline GHG emissions for SA Scope: National E3 Focus: GHG emissions in a “No Climate Policy” Scenario + Methodology Funders: UNEP
GDP & Population
Fuels Prices
SA TIMES energy model
Least cost energy mix
UNCERTAINTY
Technology Costs
GHG Emissions Projection
Monte Carlo algorithm
SA TIMES Model
(SATIM)
Expert Elicitation
Combined Elicited Distributions

## Slide 24: Project: Potential Role of Natural Gas in SA Scope: National E3 Focus: Natural Gas demand and supply Funders: FCO, ERC
Without a GHG constraint, very limited role for gas above a gas price of USD11/Mbtu
Significant variation in uptake driven by different GDP growth rates
Notes: Uncertainty analysis of GDP growth, technology costs, fuel costs
GHG unconstrained and constrained scenarios
1000 model runs to test the impact of uncertainty – which are the critical factors which make a difference?
Using a full systems model picks up on interesting systemic effects - e.g. the use of natural gas as a transport fuel rather than GTL

## Slide 25: Project: Potential Role of Natural Gas in SA Scope: National E3 Focus: Natural Gas demand and supply Funders: FCO, ERC
With a GHG constraint,a much more diversified role for gas above USD11/Mbtu
Smaller range of uptake due to the GHG constraint – less response to GDP growth

## Slide 26: Project: Stochastic Programming: Uncertainty on CO2 Constraint Scope: National E3 Focus: CO2 emissions, impact on Electricity Price+Methodology Funders: CIFF via MAPS

## Slide 27
Future 1: Sustained electricity price increase
~R400bn additional electricity sector investment requirement
Job and welfare threats
Future 2: No electricity price increase
Opportunities for growth from over supply of electricity
In 2030
Project: Socioeconomic Implications of SA’s Nuclear Build Plan Scope: National E3 Focus: Electricity, Socio-economics Funders: ELA

## Slide 28: Project: Thirsty Energy Scope: National E3 Focus: Energy and Water Nexus focusing on Energy Supply (excl. biofuels) + Methodology Development Funders: World Bank Collaborators: Aurecon, Decisionware

## Slide 29
Thank you!
brunomerven@gmail.com