## Slide 1: Modelling Energy Demand in South Africa Energy Systems Research Group – University of Cape Town

## Slide 2: Overview of Transport in SATIMGE
Projected demand for freight services

## Slide 3: SATIM Full Sector Energy Systems Model (rough sketch)
Primary Supply
Coal
Crude Oil
Natural Gas
Transformation
Liquid Fuels
Electricity
Transmission and Distribution
Coal
Liquid
Gas
Electricity
Demand
Heating Demand
Veh-km Demand
Coal Transport
Coal Power Plants
Coal Boiler
Coal Mines
Liquid Fuels
Gas Power Plants
Distribution
Gas Boiler
Crude Imports
RE Power Plants
Crude Refineries
ICE Vehicle
Gas Network
Gas Imports
Pipeline
Coal to Liquids Plant
Electric Vehicle
Electricity Network
Gas Imports
LNG Terminal
Liquid fuels Imports
Notes: This slide shows what we call a Reference Energy Diagram of the energy system. It has more detail than the energy balance in that we also describe which energy services are met by the energy commodities.
1. The demand for energy services are more strongly linked to the economic drivers: GDP, population and income.
2. Different carriers can be used to meet the same energy service demand.
With a detailed description of how energy is produced and consumed, we use an optimization approach to compute the least-cost technology mix (both on supply and demand) given scenario based, “out of sample” projections of:
The energy service demand of the economy given
retirement of the existing stock of energy equipment (coal power plants),
new technology costs, and
Fuel prices
Policy levers (e.g. GHG reduction goal)

## Slide 4: SATIM Transport Vechicles
(1): BRT: Bus Rapid Transport; (2): Metro: Metropolitan i.e. intra‐city; (3): Used for Coastal & Inland Navigation; * Internal Combustion Engine; #: Battery Electric for Road Vehicles; HCV1: Medium commercial vehicle of 3 000–7 500kg GVM; HCV 2: Heavy commercial vehicle of 7 501–12 000 kg GVM; HCV 6: Heavy commercial vehicle of 24 001–32 000 kg GVM. SUV: Sport Utility Vehicle (usually 4X4 and >1ton in mass)
Notes: This slide shows the detail of the vehicle park that makes up the transport sector demand

## Slide 5: Passenger Transport is quite complicated
Source: S. Armenia et al.

## Slide 6: Common Approaches
Population
Total Pkm
Mode Share
Pkm by Mode
Occupancy
Vkm by Mode
Check
Vehicle parc
Mileage
Check
Km per person per year
Population
Sum across modes
Total Pkm
Occupancy
Pkm by Mode
Mileage
Total Vkm
Start
Km per person per year
1.
Start
Vehicle Parc (all modes)
2.
To TIMES Model

## Slide 7: Approach 1: Problem
Assumes that km per person per year is independent of mode share
Population
Total Pkm
Mode Share
Pkm by Mode
Occupancy
Vkm by Mode
Check
Vehicle parc
Mileage
Start
Km per person per year
1.

## Slide 8: Approach 2: Problem
Different modes are projected independently
Check
Km per person per year
Population
Sum across modes
Total Pkm
Occupancy
Pkm by Mode
Mileage
Total Vkm
Start
Vehicle Parc (all modes)
2.

## Slide 9: Approach adopted: 2 with fixed travel time budget
Inspired by Schafer & Victor (2000)
Use travel time budget in combination with mode speeds to ensure inter-modal consistency

## Slide 10: Adopted Approach
Start
Vehicle ownership (private)
Mileage + Occupancy
pkm in private
Time spent in private travel
Priv.Speed
Time budget
Time spent in public travel
Pub.Speed
pkm in public
Check
Mode Share

## Slide 11: Saturation comes from income group population
Fraction Pass. Car Owners
Fraction No Car
Income Group Low
Income Group Medium
Income Group High
Saturation Occurs when Net Transition to Income Group High stabilises at a low rate
Motorisation is highly correlated to GDP/Capita. Often modelled by a Gompertz Curve (see Kenworthy & Townsend,)

## Slide 12: Income Group Behaviour

## Slide 13: Illustrative BRT (Bus Rapid Transit) Case
People with access to a private vehicle
People without access to a private vehicle

## Slide 14: Overall Mode Share (pkm)

## Slide 15: SANEDI Study Results: Projecting Energy Demand Step 1

## Slide 16: Results: Projecting Energy Demand Step 2
SANEDI report can be downloaded from ERC Website
And so can the TIMES model and the accompanying spreadsheets

## Slide 17: Still a Lot of work left to do:
1. Household budget constraint
Schafer & Victor (2000)
2007 SAM

## Slide 18: Still a Lot of Work to do:
Vehicle km
by mode
Household
Income proj.
Priv. Vehicle
ownership
Transport
/Energy Policy
Taxes and
Subsidies
Relative cost
of techs proj.
Occupancy
proj.
Annual Mileage
proj.
Relative speed
of modes
Relative cost
of modes
Mode Share
/pkm proj.
Fuel price
proj.
2. Endogenising modal choice based on relative cost or utility: From System’s point of view of Traveler’s point of view?

## Slide 19
Questions?

## Slide 20: Challenge: Data is Sparse
Detailed
Vehicle Parc
NAAMSA
Vehicle Sales
Enatis
veh. pop
Vehicle km
Fuel
Consumption
SAPIA/EB
Fuel sales
P-km, T-km/
Mode-share
Natmap/SOL
P-km, t-km
We have
We want

## Slide 21: Calibration Process
Vehicle Parc
Model
Vehicle km
Fuel
Consumption
P-km, T-km/
Mode-share
Scrapping
Factor
Vehicle
Mileage/Decay
Fuel Economy/
Improvement
Occupancy
NAAMSA
Vehicle Sales
Enatis Check
SAPIA/EB
Check
Natmap/SOL
Check

## Slide 22: Some Calibration Results: Car Parc
Cars
Minibus
Light Duty Vehicles

## Slide 23: Some Calibration Results: Fuel Sales (litres)
Diesel
Gasoline

## Slide 24: Some Calibration Results: Vehicle Mileage and Fuel Consumption
Years
Diesel Vehicles